## Slide 1: Lecture 7-1 : Manycore GPU Programming with CUDA
Courtesy : Prof. Christopher Cooper’s and Prof. Chowdhury’s course note slides are used in this lecture note

## Slide 2: Moore’s Law
Transistor count of integrated circuits doubles every two years

## Slide 3: The Need of Multicore Architecture
Hard to design high clock speed (frequency)
  power consumption and heat generation : too high
  # of cores may still increase

## Slide 4: Parallelism
Task parallelism
  Distributing different tasks across multiple processors or threads
  Amount of parallelization is proportional to the number of independent tasks
  Suitable to CPU
Data parallelism
  Same task are performed on different subsets of same data
  Amount of parallelization is proportional to the input data size
  Suitable to GPU

## Slide 5: SIMT
The architecture of GPU is based on SIMT
Single Instruction, Multiple Threads
  Executes the same instruction across multiple threads
  A group of threads is controlled by a control unit
    E.g. 32 threads (=warp)
  Divergent workflow among threads in a group is allowed
    With a little performance penalty (e.g. work serialization)

## Slide 6: SIMT in GPUs
A GPU consists of many Streaming Multiprocessors (SMs)
Each SM executes a warp, which is a group of typically 32 threads
These threads run the same instruction at the same time, just like SIMD, but
  Each thread has its own program counter and registers
  Threads can diverge, allowing for some conditional execution
  This gives SIMT flexibility over SIMD, which usually requires all operations to be strictly identical per cycle

## Slide 7: Warp Divergence
If threads in the same warp follows different branch paths, each branch will be serially executed.
Warp divergence can easily result in bad performance. Avoid branches!
[Source: from Prof. Duksu Kim’s lecture slides]

## Slide 8: Many-core GPUs
Motivation
  Originally driven by the insatiable market demand for realtime, high-definition 3D graphics
  programmable GPU has evolved into a highly parallel, multithreaded, manycore processor with tremendous computational horsepower and very high memory bandwidth
  GPGPU
    General Purpose computing on GPU (Graphical Processing Unit)
    Utilization of GPU (typically handles computations for graphics) to perform general purpose computation (traditionally handled by CPU)

## Slide 9: Processor : Multicore vs Many-core
Multicore direction (CPU) : 2~8 cores
  Typically handles general purpose computation
  seeks to maintain/increase the execution speed of sequential programs
  Complex : out-of-order, multiple instruction issue, branch prediction, pipelining, large cache, …
  while moving into multiple cores
  Ex) Intel i7 has 4 cores (hexa-core was released recently)
Many-core direction (GPU) : 100~3000 cores
  Focus on the execution throughput of parallel applications
  Simple : in order, single instruction issue
  Large number of smaller cores

## Slide 10: Many-core GPU
NVIDIA GTX 780 Ti
  Around 3000 cores on single chip
  Economic price : mass-market product (around $700)
  Easy to program : CUDA

## Slide 12: GPU
Specially designed for highly parallel applications
  Programmable using high level languages (C/C++)
  Supports standard 32-bit floating point precision
  Lots of GFLOPS

## Slide 13: GPU
Fast processing must come with high bandwidth!
Simpler memory models and fewer constraints allow high bandwidth
Memory bandwidth
  the rate at which data can be read from or stored into memory by a processor

## Slide 14: GPU
GPU is specialized for
  Compute-intensive
  Highly data parallel computation
    the same program is executed on many data elements in parallel
    Ex) matrix computation
  More transistors devoted to data processing rather than data caching and flow control
What graphics rendering needs?
  Geometry(vertex) + Pixel processing
Motivates many application developers to move the computationally intensive parts of their software to GPUs for execution

## Slide 15: Applications
3D rendering
  large sets of pixels and vertices are mapped to parallel threads.
image and media processing applications such as post-processing of rendered images, video encoding and decoding, image scaling, stereo vision, and pattern recognition
  can map image blocks and pixels to parallel processing threads.
many other kinds of algorithms are accelerated by data-parallel processing
  from general signal processing or physics simulation to computational finance or computational biology.

## Slide 16: CPU vs GPU
CPU: Optimized for sequential code performance
  sophisticated control logic
    to allow instructions from single thread to execute in parallel or even out-of-order
    branch prediction
  large cache memory
    to reduce the instruction and data access latencies
  Powerful ALU : reduced operation latency
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU
CPU vs GPU : fundamentally different design philosophies

## Slide 17: CPU vs GPU
GPU: Optimized for execution throughput of multiple threads
  Originally for fast (3D) video game
    Requires a massive number of floating-point calculations per frame
  Minimize control logic and cache memory
    Much more chip area is dedicated to the floating-point calculations
    Boost memory throughput
  Energy Efficient ALU
  Designed as (data parallel) numeric computing engines
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU
CPU vs GPU : fundamentally different design philosophies

## Slide 18: GPU Architecture
GPUs consist of many simple cores
Array of highly threaded streaming multiprocessors (SMs)
Two or more SMs form a buliding block.

## Slide 19: GPU chip design
GPU core is stream processor
Stream processors are grouped in stream multiprocessors
  SM is basically a SIMD processor (single instruction multiple data)

## Slide 20: CPU vs GPU
GPU
  GPU designed for many simple tasks
  Maximize throughput (# of tasks in fixed time)
CPU
  Minimize latency (time to complete a task)

## Slide 21: Winning Applications Use Both CPU and GPU
GPUs will not perform well on some tasks on which CPUs perform well
Use both CPUs and GPUs
  Executing essentially sequential parts on CPU
  Numerically intensive parts on GPU
CUDA
  Introduced by NVIDIA in 2007
  Designed to support joint CPU/GPU execution of applications

## Slide 22: Popularity of GPUs
Performance
Cost
large marketplace & customer population
Practical factors and easy accessibility
  GE MRI with {clusters and GPU}
Support of IEEE floating-point standard
CUDA
  Programmer can use C/C++ programming tools
  No longer go through complex graphics interface

## Slide 23: Why more parallelism?
Applications will continue to demand increased speed
A good implementation on GPU can achieve more than 100 times speedup over sequential execution
Supercomputing applications
  Any applications that require data-parallel calculations such as
  matrix calculations

## Slide 24: CUDA (Computer Unified Device Architecture)
Parallel Computing Framework Developed by NVIDIA (working only on NVIDIA cards)
Introduced in 2006
General Purpose Programming Model
  GPGPU (General Purpose GPU)
  Offers a computing API
  Explicit GPU memory management
Goal
  Develop application SW that transparently scales its parallelism to leverage the increasing number of processor cores

## Slide 25: CUDA enabled GPUs
warp : group of threads where multiprocessor executes the same instruction at each clock cycle

## Slide 26: Compute Capability
general specifications and features of compute device
Defined by major revision number and minor revision number
  Ex) 1.3 , 2.1 , 3.5 , 5.0
  5 : maxwell architecture
  3 : Kepler architecture
  2 : Fermi architecture
  1 : Tesla architecture

## Slide 27: CUDA – Main Features
C/C++ with extensions
Heterogeneous
programming model
Operates in CPU(host)
and GPU (device)

## Slide 28: CUDA Device and Threads
Device
  Is a coprocessor to the CPU or host
  Has access to DRAM (device memory)
  Runs many threadsin parallel
  Is typically a GPUbut can also be another type of parallel processing device
Data-parallel portions of an application are expressed as device kernels which run on many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight (little overhead for creation)
  GPU needs 1000s of threads for full efficiency
    (multicore CPU needs only a few)

## Slide 29: Processing Flow

## Slide 30: Example 1: Hello world
#include <stdio.h>
void hello_world(void) {
printf(“Hello World\n”);
}
int main (void) {
hello_world();
return 0;
}

## Slide 31: Example 1: CUDA Hello world
#include <stdio.h>
__global__ void hello_world(void) {
printf(“Hello World\n”);
}
int main (void) {
hello_world<<<1,5>>>();
cudaDeviceSynchronize();
return 0;
}

## Slide 32: Compile and Run
output
  Hello World
  Hello World
  Hello World
  Hello World
  Hello World

## Slide 33: C Language Extensions
Function Type Qualifiers
  __global__
    executed on the device (GPU)
    callable from the host (CPU) only
    functions should have void return type
    any call to a __global__ function must specify the
    execution configuration for that call

## Slide 34: Grid, Block, Thread
Tesla S2050, Geforce 580
  max. block size of each
  Dim per grid
  65535x65535x1
  max. thread size of
  each Dim per block
  1024x1024x64
  max. # of threads per block
  1024

## Slide 35: C Language Extensions
Execution configuration
  <<<blocksPerGrid,threadsPerBlock>>>
  <<<1,1>>>
  <<<65535,1024>
  dim3 blocksPerGrid(65535,65535,1)
  dim3 threadsPerBlock(1024,1,1)
  <<<blocksPerGrid,threadsPerBlock>>>

## Slide 36: C Language Extensions
Built-in Variables
  blockIdx = (blockIdx.x, blockIdx.y, blockIdx.z)
  three unsigned integers, uint3
  threadIdx = (threadIdx.x, threadIdx.y, threadIdx.z)
  three unsigned integers, uint3
  blockDim: the number of threads in a block
  gridDim: the number of blocks in a grid
Built-in Vector types
  dim3:
    Integer vector type based on unit3
    used to specify dimensions

## Slide 37: Technical Specs per Compute Capability
[The table image is from Prof. Duksu Kim’s lecture note]

## Slide 38
#include <stdio.h>
__global__ void exec_conf(void) {
int ix = threadIdx.x + blockIdx.x * blockDim.x;
printf("gridDim = (%d,%d,%d), blockDim = (%d,%d,%d)\n",
gridDim.x,gridDim.y,gridDim.z,
blockDim.x,blockDim.y,blockDim.z);
printf("blockIdx = (%d,%d,%d), threadIdx = (%d,%d,%d), arrayIdx %d\n",
blockIdx.x,blockIdx.y,blockIdx.z,
threadIdx.x,threadIdx.y,threadIdx.z, ix);
}
int main (void) {
exec_conf<<<2,3>>>();
cudaDeviceSynchronize();
return 0;
}

## Slide 39: Compile and Run
Output
gridDim = (2,1,1), blockDim = (3,1,1)
gridDim = (2,1,1), blockDim = (3,1,1)
gridDim = (2,1,1), blockDim = (3,1,1)
gridDim = (2,1,1), blockDim = (3,1,1)
gridDim = (2,1,1), blockDim = (3,1,1)
gridDim = (2,1,1), blockDim = (3,1,1)
blockIdx = (0,0,0), threadIdx = (0,0,0), arrayIdx = 0
blockIdx = (0,0,0), threadIdx = (1,0,0), arrayIdx = 1
blockIdx = (0,0,0), threadIdx = (2,0,0), arrayIdx = 2
blockIdx = (1,0,0), threadIdx = (0,0,0), arrayIdx = 3
blockIdx = (1,0,0), threadIdx = (1,0,0), arrayIdx = 4
blockIdx = (1,0,0), threadIdx = (2,0,0), arrayIdx = 5

## Slide 40
#include <stdio.h>
__global__ void exec_conf(void) {
int ix = threadIdx.x + blockIdx.x * blockDim.x;
int iy = threadIdx.y + blockIdx.y * blockDim.y;
printf("gridDim = (%d,%d,%d), blockDim = (%d,%d,%d)\n",
gridDim.x,gridDim.y,gridDim.z,
blockDim.x,blockDim.y,blockDim.z);
printf("blockIdx = (%d,%d,%d), threadIdx = (%d,%d,%d), arrayIdx=(%d,%d)\n",
blockIdx.x,blockIdx.y,blockIdx.z,
threadIdx.x,threadIdx.y,threadIdx.z, ix,iy);
}
int main (void) {
dim3 blocks(2,2,1);
dim3 threads(2,2,2);
exec_conf<<<blocks,threads>>>();
cudaDeviceSynchronize();
return 0;
}

## Slide 41: Example 3: Vector sum
int main (void) {
int a[N], b[N], c[N];
for (int i=0; i<N; i++) {
a[i] = -i;
b[i] = i * i;
}
add (a, b, c);
for (int i=0; i<N; i++) {
printf("%d + %d = %d\n", a[i],b[i],c[i]);
}
return 0;
}
#include <stdio.h>
const int N=128;
void add(int *a, int *b, int *c) {
for (int i=0; i<N; i++) {
c[i] = a[i] + b[i];
}
}

## Slide 42: Example 3: Vector sum
#include <stdio.h>
const int N=10;
__global__ void add(int *a, int *b, int *c) {
int tid = threadIdx.x;
c[tid] = a[tid] + b[tid];
}

## Slide 43
int main (void) {
int a[N], b[N], c[N];
int *dev_a, *dev_b, *dev_c;
cudaMalloc( (void**)&dev_a, N * sizeof(int) );
cudaMalloc( (void**)&dev_b, N * sizeof(int) );
cudaMalloc( (void**)&dev_c, N * sizeof(int) );
for (int i=0; i<N; i++) {
a[i] = -i; b[i] = i * i;
}
cudaMemcpy ( dev_a, a, N * sizeof(int), cudaMemcpyHostToDevice );
cudaMemcpy ( dev_b, b, N * sizeof(int), cudaMemcpyHostToDevice );
add<<<1,N>>>(dev_a, dev_b, dev_c);
// add<<<N,1>>>(dev_a, dev_b, dev_c);
// add<<<128,128>>>(dev_a, dev_b, dev_c);
cudaMemcpy(c, dev_c, N * sizeof(int),cudaMemcpyDeviceToHost );
for (int i=0; i<N; i++) {
printf("%d + %d = %d\n", a[i],b[i],c[i]);
}
cudaFree (dev_a); cudaFree (dev_b); cudaFree (dev_c);
return 0;
}

## Slide 44: Compile and Run
Output
0 + 0 = 0
-1 + 1 = 0
-2 + 4 = 2
-3 + 9 = 6
-4 + 16 = 12
-5 + 25 = 20
-6 + 36 = 30
-7 + 49 = 42
-8 + 64 = 56
-9 + 81 = 72