## Slide 1: Lecture 2-1 : Introduction to Multicore Computing
Bong-Soo Sohn
Associate Professor
School of Computer Science and Engineering
Chung-Ang University

## Slide 2: Multicore Processor
A single computing component with two or more independent cores
  Core (CPU): computing unit that reads/executes program instructions
  Ex) dual-core, quad-core, hexa-core, octa-core, …
  share cache or not
  symmetric or asymmetric
  Ex) intel i9-13900K (link)
Intel Quad-core processors (Sandy Bridge)

## Slide 3: Intel Multicore CPU (Recent)
Performance Cores vs Efficiency Cores
[source (2024.3): enuri.com]
Intel i9-13900K
L3 cache (shared)

## Slide 4: Apple CPUs: M1 (2021) , M3 (2023)
CPU clock rate: 3.2GHz (M1) , 4.05GHz (M3)

## Slide 5: Apple M4 CPU (2024)

## Slide 6: Apple Unified Memory
Unified memory
  CPU, GPU, NPU share memory on a single chip
  +: efficient
  -: cannot be changed/replaced after production.

## Slide 7: Multicore Processor
Multiple cores run multiple instructions at the same time (concurrently)
Increase overall program speed (performance)
performance gained by multi-core processor
  strongly dependent on the software algorithms and implementation.
desktop PCs, mobile devices, servers

## Slide 8: Manycore processor (GPU)
multi-core architectures with an especially high number of cores (thounds)
  Ex) nVidia GeForce RTX 3080 Ti (2021.06)

## Slide 9: Manycore processor (GPU)
CUDA
  Compute Unified Device Architecture
  parallel computing platform and programming model created by NVIDIA and implemented by the graphics processing units (GPUs) that they produce
  GPGPU (General Purpose Graphics Processing Unit)
OpenCL
  Open Standard parallel programming platform

## Slide 10: Parallel Applications
Image and video processing
  Encoding, editing, filtering
3D graphics (rendering, animation)
3D gaming
Simulation
  e.g. protein folding, climate modeling
Machine learning, deep learning

## Slide 11: Thread/Process
Both
  Independent sequence of execution
Process
  run in separate memory space
Thread
  Run in shared memory space in a process
  One process may have multiple threads
Multithreaded Program
  a program running with multiple threads that is executed simultaneously
A process with two threads of execution on a single processor

## Slide 12: What is Parallel Computing?
Parallel computing
  using multiple processors in parallel to solve problems more quickly than with a single processor
Examples of parallel machines:
  A cluster computer that contains multiple PCs combined together with a high speed network
  A shared memory multiprocessor by connecting multiple processors to a single memory system
  A Chip Multi-Processor (CMP) contains multiple processors (called cores) on a single chip
Concurrent execution comes from desire for performance; unlike the inherent concurrency in a multi-user distributed system

## Slide 13: Parallelism vs Concurrency
Parallel Programming
  Using additional computational resources to produce an answer faster
  Problem of using extra resources effectively?
  Example
    summing up all the numbers in an array with multiple n processors

## Slide 14: Parallelism vs Concurrency
Concurrent Programming
  Correctly and efficiently controlling access by multiple threads to shared resources
  Problem of preventing a bad interleaving of operations from different threads
  Example
    Implementation of dictionary with hashtable
      operations insert, update, lookup, delete occur simultaneously (concurrently)
      Multiple threads access the same hashtable
    Web Visit Counter

## Slide 15
Concurrency (Concurrent Programming)
  A program is organized so multiple tasks can make progress during overlapping time periods
  (but, not necessarily at the exact same instant)
  Logically simultaneous execution
  Can be interleaved execution on a single CPU
  Goal: managing many tasks
Parallelism (Parallel Programming)
  Multiple tasks execute at the exact same time
  Physically simultaneous execution
  Requires multiple cores/processors
  Goal: speed up computation
Concurrency is about dealing with lots of things at once.
Parallelism is about doing lots of things at once.
- Rob Pike (Co-creator of Go language)

## Slide 16: Parallelism vs Concurrency
Often Used interchangeably
In practice, the distinction between parallelism and concurrency is not absolute
Many multithreaded programs have aspects of both

## Slide 17: Parallel Programming Techniques
Shared Memory
  OpenMP, pthreads
Distributed Memory
  MPI
Distributed/Shared Memory
  Hybrid (MPI+OpenMP)
GPU Parallel Programming
  CUDA programming (NVIDIA)
  OpenCL

## Slide 18: Parallel Processing Systems
Small-Scale Multicore Environment
  Notebook, Workstation, Server
  OS supports multicore
  POSIX threads (pthread) , win32 thread
  GPGPU-based supercomputer
  Development of CUDA/OpenCL/GPGPU
Large-Scale Multicore Environment
  Supercomputer : more than 10,000 cores
  Clusters
  Servers
  Grid Computing

## Slide 19: Parallel Computing vs. Distributed Computing
Parallel Computing
  all processors may have access to a shared memory to exchange information between processors.
  more tightly coupled to multi-threading
Distributed Computing
  multiple computers communicate through network
  each processor has its own private memory
  (distributed memory).
  executing sub-tasks on different machines and then merging the results.

## Slide 20: Parallel Computing vs. Distributed Computing
No Clear Distinction
Distributed Computing
Parallel Computing

## Slide 21: Cluster Computing vs. Grid Computing
Cluster Computing
  a set of loosely connected computers that work together so that in many respects they can be viewed as a single system
  good price / performance
  memory not shared
Grid Computing
  federation of computer resources from multiple locations to reach a common goal (a large scale distributed system)
  grids tend to be more loosely coupled, heterogeneous, and geographically dispersed

## Slide 22: Cluster Computing vs. Grid Computing

## Slide 23: Example of Grid Computing (Folding@Home)

## Slide 24: Example of Grid Computing (Folding@Home)

## Slide 25: Cloud Computing
shares networked computing resources rather than having local servers or personal devices to handle applications.
“Cloud” is used as a metaphor for “Internet"
meaning "a type of Internet-based computing,“
different services - such as servers, storage and applications - are delivered to an user’s computers and smart phones through the Internet.

## Slide 26: Good Parallel Program
Writing good parallel programs
  Correct (Result)
  Good Performance
  Scalability
  Load Balance
  Portability
  Hardware Specific Utilization

## Slide 27: Moore’s Law : Review
Doubling of the number of transistors on integrated circuits roughly every two years.
Microprocessors have become smaller, denser, and more powerful.
processing speed, memory capacity, sensors and even the number and size of pixels in digital cameras.All of these are improving at (roughly) exponential rates

## Slide 28: Computer Hardware Trend
Chip density is continuing
increase ~2x every 2years
  Clock speed is not
  (in high clock speed, power
  consumption and heat generation
  is too high to be tolerated.)
  # of cores may double instead
No more hidden parallelism
(ILP;instruction level parallelism)
to be found
Transistor# still rising
Clock speed flattening sharply
Need Multicore programming!
Source: Intel, Microsoft (Sutter) and Stanford (Olukotun, Hammond)

## Slide 30: Examples of Parallel Computer
Chip MultiProcessor (CMP)
  Intel Core Duo
  AMD Dual Core
Symmetric Multiprocessor (SMP)
  Sun Fire E25K
Heterogeneous Chips
  Cell Processor
Clusters
Supercomputers

## Slide 31: Generic SMP
Symmetric MultiProcessor (SMP) System
  multiprocessor hardware architecture
  two or more identical processors are connected to a single shared memory
  controlled by a single OS instance
  Most common multiprocessor systems today use an SMP architecture
  Both Multicore and multi-CPU
  Single logical memory image
  Shared bus often bottleneck

## Slide 32: GPGPU : NVIDIA GPU
Tesla K20
  GPU : 1 Kepler GK110
  2496 cores; 706MHz
  Tpeak 3.52Tflop/s – 32bit floating point
  Tpeak 1.17Tflop/s – 64bit floating point
GTX 680
  1536 CUDA cores; 1.0GHz

## Slide 33: Hybrid Programming Model
Main CPU performs hard to parallelize portion
Attached processor (GPU) performs compute intensive parts

## Slide 34: Why writing (fast) parallel programs is hard

## Slide 35: Principles of Parallel Computing
Finding enough parallelism (Amdahl’s Law)
granularity
Locality
Load balance
Coordination and synchronization
All of these things makes parallel programming even harder than sequential programming.

## Slide 36: Overhead of Parallelism
Given enough parallel work, this is the biggest barrier to getting desired speedup
Parallelism overheads include:
  cost of starting a thread or process
  cost of communicating shared data
  cost of synchronizing
  extra (redundant) computation
Each of these can be in the range of milliseconds (=millions of flops) on some systems
Tradeoff: Algorithm needs sufficiently large units of work to run fast in parallel (I.e. large granularity), but not so large that there is not enough parallel work

## Slide 37: Summary
All computers are now parallel computers!
Multi-core processors represent an important new trend in computer architecture.
  Decreased power consumption and heat generation.
  Minimized wire lengths and interconnect latencies.
They enable true thread-level parallelism with great energy efficiency and scalability.

## Slide 38: Summary
To utilize their full potential, applications will need to move from a single to a multi-threaded model.
  Parallel programming techniques likely to gain importance.
  Hardware/Software
the software industry needs to get back into the state where existing applications run faster on new hardware.